## Slide 1
01
Approach
Compact recognition designed for embedded inference
Algorithm / model
A 5-block depthwise-separable CNN (16->24->32->48->64) with learned 6x6 per-channel spatial pooling and a Dense(17) classifier.
Why this model
Depthwise convolutions provide strong image features with few parameters; learned spatial pooling preserves useful sign location cues while keeping flash and RAM usage low.
AI ARENA 2026

## Slide 2
02
Training
Orientation-aware learning on the supplied dataset
How it was trained
48x48 RGB images; class-aware oversampling; +/-6 degree rotation, translation, zoom, brightness and contrast augmentation; class weights; Adam with cosine learning-rate decay; label smoothing 0.05 and light MixUp (alpha 0.10).
Training / validation result
Quantization-aware training (25 epochs) evaluated every checkpoint as INT8. The selected checkpoint achieved 352/364 correct on validation: 96.70%.
AI ARENA 2026

## Slide 3
03
Optimization
Full-integer deployment without measured accuracy loss
Technique
Quantization-aware training followed by full-integer INT8 TFLite conversion with INT8 input and output. The best checkpoint was selected using exact INT8 validation accuracy.
Model size
Before: 234,708-byte Keras artifact. After: 30,168-byte TFLite model (87.1% smaller).
Accuracy impact
Selected checkpoint before conversion: 96.70%. INT8 model after conversion: 96.70% (352/364). No measured validation loss.
AI ARENA 2026

## Slide 4
04
Embedded Deployment
TensorFlow Lite Micro integrated with Zephyr RTOS
Zephyr integration
The TFLite model is embedded as a C byte array. A static TFLM interpreter and 40 KB tensor arena register only the required operators. Firmware receives a 6,912-byte RGB frame over UART and returns the official class ID.
Running in QEMU
Build the Zephyr qemu_x86 target, boot it with QEMU, then use qemu_uart_test.py to send the 0xAA 0x55 marker plus image bytes and read the predicted ID. Predictions were checked against desktop TFLite output.
AI ARENA 2026

## Slide 5
05
Performance on Validation Set in QEMU
Measured with the deployed v16 INT8 firmware
Accuracy
352/364 correct (96.70%), with exact QEMU prediction parity on the tested validation images.
Model size
30,168 bytes (29.5 KB), 11,417 parameters.
RAM usage
TFLM tensor arena: 28,436 / 40,960 bytes used. Zephyr build RAM: 279,164 bytes.
Inference time
Approximately 82-106 ms per frame in qemu_x86. QEMU timing is emulated and is not physical ESP32-S3 latency.
AI ARENA 2026